## Slide 1: Tutorial 2 - Project Development Flow
Prof. Ren-Shuo Liu Willie Tsai

## Slide 2: Project Development Flow
TensorFlow
Model
Development
Firmware
Development
Run / Update
Application
On WE-I
Download img file
Debug
Convert
Stage | TensorFlow Model Development | Firmware Development | Run / Update Application On WE-I
Tool | Anaconda Cygwin | Cygwin Metaware or ARC GNU VirtualBox (Ubuntu 20.04) | Tera Term USB Micro
Language | Python 3 | C language C++ language | 

## Slide 3: Project Development Flow
TensorFlow
Model
Development
Firmware
Development
Run / Update
Application
On WE-I
Download img file
Debug
Convert
Stage | TensorFlow Model Development | Firmware Development | Run / Update Application On WE-I
Tool | Anaconda Cygwin | Cygwin Metaware or ARC GNU VirtualBox (Ubuntu 20.04) | Tera Term USB Micro
Language | Python 3 | C language C++ language | 

## Slide 4: Firmware Development
Program
Code
Compile
Project
Create elf and map file
Convert img file
Any editor for C or C++
Use any tool which supports “make” command
Toolchain: Metaware or GNU
VirtualBox
for Ubuntu

## Slide 5: Download and Set up SDK
Use Cygwin and “cd” to your working path
Download SDK from Himax Github git clone https://github.com/HimaxWiseEyePlus/himax_tflm.git
Go to the root of Himax SDK cd himax_tflm
Download third party file (3 packages) make download
Download SDK from Synopsys Github git clone 測試中
Go into folder “test_project” you will see folder “src” and “inc” makefile is already setting compiler .c and .cc file in folder “src”, and include file in folder “inc” “src” folder: always keep your .c and .cc file in here. “inc” folder: always keep your .h in here.
c file: c language
cc file: c++ language

## Slide 6: Program Code
Copy a template project and rename. Because makefile instruction, you can only create the project at same path level. Copy “Synopsys_Project/Example Project/person_detection_int8” To “Synopsys_Project/User Project/test_project”
Go into folder “test_project” you will see folder “src” and “inc” makefile is already setting compiler .c and .cc file in folder “src”, and include file in folder “inc” “src” folder: always keep your .c and .cc file in here. “inc” folder: always keep your .h in here.
c file: c language
cc file: c++ language

## Slide 7: Project Development Flow
TensorFlow
Model
Development
Firmware
Development
Run / Update
Application
On WE-I
Download img file
Debug
Convert
Stage | TensorFlow Model Development | Firmware Development | Run / Update Application On WE-I
Tool | Anaconda Cygwin | Cygwin Metaware or ARC GNU VirtualBox (Ubuntu 20.04) | Tera Term USB Micro
Language | Python 3 | C language C++ language | 

## Slide 8: Run / Update Application On WE-I
WE-I
Reset
Any Data from SPI in 0.3 sec
Running
Application
Mode
Update
Application
Mode
Yes
No

## Slide 9: Update Application On WE-I
WE-I
Reset
Any Data from SPI in 0.3 sec
Update
Application
Mode
Yes
Receive and Update Application
Key “1”
Reset
and
run
WE-I
Prepare
img file
Transmit
Img file
by Xmodem
Tera Term

## Slide 10: Update Application On WE-I Connect WE-I with Tera Term
Connect WE-I and PC by USB Cable
Check your WE-I usb port number Device Manager > Ports(COM & LPT) > USB Serial Port (COMx) x: This is your WE-I usb port number
Open tera term and select “COMx: USB Serial Port (COMx)”
Tera term Setting > Com Port > Change Baud to 115200, and keep other setting.
Reset WE-I by pushing SW2, you will see startup information on tera term.

## Slide 11: Update Application On WE-I Enable Update Application Mode with Tera Term
Finish to connect WE-I with Tera Term
Click on any display area
Keep to press key “1” on the keyboard, and reset WE-I.
WE-I will start to receive img file by Xmodem
Tera term File > Transmit > XMODEM > Transmit > select img file
Wait for Transmit
Reset and run your application

## Slide 12: Run Application On WE-I
Connect USB cable to power up WE-I you can also power up by 2.54 pitch connector
For debug easily, suggest to use Tera Term and print date or result
Start to develop your project, and debug your code